## Slide 1: Mechanical Keyboards
Your next hobby

## Slide 2: ‘Mechanical’ keyboard?
Aren’t all keyboards mechanical?
Non-Mech
  Membranes under keys, have a squishy feeling.
  No real tactile feedback.
  Generally lack support for n-key rollover.
Mech
  Mechanical switches under each key.
  Often combined with other higher quality parts; cases, keycaps, customized via firmware.

## Slide 3: What’s it made of?

## Slide 4: Form Factors
Full-size
Tenkeyless/TKL/80%
75%
60%
40%

## Slide 5: Layouts

## Slide 6: Switches
Components
  Upper and Lower Housing
  Stem
  Metal contacts
  Spring
Cherry MX is a common style
Distinguished by color

## Slide 7: Switch Types
The keyboard feel & sound
Linear
  smooth, quiet, no ‘bump’, faster feel, bottom out.
Tactile
  a bump midway through stroke / actuation-point
Clicky
  a bump & click midway through stroke / actuation-point
Others…
  Buckling Spring, Alps, Topre

## Slide 8: Case & Plates
Cases come in plastic, acrylic, aluminum, brass, etc.
Plates come in plastic, aluminum, brass, steel, etc.

## Slide 9: PCB
Match the form factor
USB I/O / Bluetooth
uController - Firmware (QMK)
Hot-Swap PCB
  no soldering, swap switches in/out
Standard PCB w/ SMT
  solder switches with some options on placement
Through hole or no PCB
  no SMT, harder to find
  hand-wired
Solder PCB
Hot-Swap Socket (bottom)

## Slide 10: Build Tools / Parts
Hot-Swap Style
Soldering Station
Screwdriver Set
Solder Style
Switches
Keycaps
Keycaps
Switches
Case/PCB/Plate
Tweezers
Stabilizers

## Slide 11: Keycaps

## Slide 12: Appendix

## Slide 13: Switch Properties
Cherry MX Blue
Switch | Feel | Activation Force (cN) | Bottom Out Force (cN) | Activation Point (mm) | Travel Distance (mm)
MX Red | Linear | 37 | 54 | 2 | 4
MX Black | Linear | 55 | 75 | 2 | 4
MX Dark Grey | Linear | 80 | 110 | 2 | 4
MX RGB Nature White | Linear | 55 | 65 | 2 | 4
MX Silent Red | Linear | 45 | 60 | 2 | 3.7
MX Silent Black | Linear | 60 | 80 | 2 | 3.7
MX Brown | Tactile | 45 | 55 | 2 | 4
MX Clear | Tactile | 50 | 85 | 2 | 4
MX Light Grey | Tactile | 67 | 110 | 2.2 | 4
MX Blue | Clicky | 55 | 60 | 2 | 4
MX Green | Clicky | 65 | 90 | 2 | 4
MX White | Clicky | 60 | 82 | 2.2 | 4
Operation Force
It's how hard you have to press the key. Operating force is measured in centinewton (cN) or gram-force (gf). 1 gf is equal to 0.98 cN, so they are almost equivalent. You can say that a switch with 0.50 cN has 0.50 gf.
Activation Point
It is the point where a keypress is recognized by the keyboard. This is measured in millimeters. It is also known as Actuation Point or Operating Position.
Total Travel Distance
It’s the distance your keycap travels until it hits the upper housing of the switch. It’s basically the distance until you bottom out. This is also measured in millimeters.
Tactile Position
Tactile position is where you feel the bump on tactile and clicky switches. On linear switches, there’s no tactile position.
Reset Point
Reset position is the distance at which the key is deactivated when released.
Kalih Speed Silver

## Slide 14: References
https://aaronbush.github.io/keyboards/builds/first.html
https://wiki.geekhack.org/index.php?title=GeekHackWiki
https://blog.wooting.nl/the-ultimate-guide-to-keyboard-layouts-and-form-factors/
https://www.keychron.com/blogs/news/keyboard-size-layout-buying-guide
https://techwithtech.com/mechanical-keyboard-parts/
https://www.daskeyboard.com/blog/mechanical-keyboard-guide/
https://www.cherrymx.de/en/